## Slide 1: Project Report AI Driven Quality Control
09.2026

## Slide 2: Table of Contents
2
  Background
3
  Project Progress
4
  Other Projects
1
  Introduction

## Slide 3: 1 Introduction About Us
Shanghai Siemens Energy High Voltage Switchgear Co., Ltd.
Shanghai Siemens Energy High Voltage Switchgear Co., Ltd., established in 2001, is a Sino-foreign joint venture jointly invested by Siemens Energy GmbH and Shanghai Electric Group Transmission & Distribution Equipment Co., Ltd. The company specializes in the research, development, manufacturing, sales, and service of high-voltage gas-insulated switchgear (GIS) rated at 52 kV and above, with products exported to 58 countries and regions.

## Slide 4: 1 Introduction Quality Control in the Company

## Slide 5: 1 Introduction Vision for Digitalization and AI Usage
Machine-Vision-based automatic Gas Insulated Switchgear (GIS) inspection
AI-assisted information summarization and key point extraction
Automation of file organization, storage, and completeness verification throughout the quality control process
AI-assisted screening and abnormality warning of quality inspection record
1
2
3
4

## Slide 6: Table of Contents
2
  Background
3
  Project Progress
4
  Other Projects
1
  Introduction

## Slide 7: 2 Background: Current Project: Generating Final Control Report with Rokid Glasses
Overview
The scope of Outgoing Quality Control (OQC) includes all outgoing GIS and modules, reproduction modules/components and pre-assembly modules in SHVS factory.
OQC is the final quality gate before packaging and shipping, mainly focused on surface finish, structural conformance with the drawing, etc..
Final Control Report (FCR) serves as a record of inspection and will be archived for 25 years.
State of art / Pain points
FCR is still done manually.
Image record and file management always takes up a lot of time.
Target:
Automation in generating the FCR.
Image capture with the help of the glasses.
Automated document archiving.
Image: Example of a final control report

## Slide 8: 2 Background Workflow of Final Quality Control
(Arrival of devices in final control area)
Go through all Inspection items.
Are there any quality issues?
Inspection start
Problem report:
Take photos and report it to Quality team
Corrective measure by corresponding department
Root cause definition
Has the Corrective measure taken effect?
Repair process documentation in Monthly Report
Start inspection again for other transportation cells
Take photos of final state and document it in Final Control Report (FCR)
Packaging and Shipping
All transportation cells inspected?
Yes
No
Go back to problem report
Yes
No
Yes
No

## Slide 9: 2 Background: Rokid AI Glasses
Specifications:
https://open.rokid.com/sprite?lang=en
Main Functions
1
Camera
2
Microphone
3
Display
4
AI Agent Functions
Hardware
Dev Platforms
AIUI Studio
UI design
Rizon
AI Agent setup
YodaOS-Sprite
OS for glasses consumer
Android Studio
UI and App design
Rokid Sprite Enterprise
SDK for glasses enterprise
Consumer System
Enterprise System
Notes: Rizon:
A low-code platform for building and deploying AI Agents by integrating its capabilities of workflows, databases, knowledgebases and plugins.
AIUI Studio:
A platform based on the AIUI (AI-Native User Interface) framework for building interactive and intuitive interfaces for the content displayed on the glasses.
SDK:
Development toolkits for both glasses and Android device, enabling data communication and completion of complex functions on both sides.

## Slide 10: Table of Contents
2
  Background
3
  Project Progress
4
  Other Projects
1
  Introduction

## Slide 11: 3 Project Progress Workflow of generating FCR with glasses
2 Save project and device information
Device model Project No.
Bay No. Batch No.
Drawing pages Module symbols
3 Load inspection items based on device model
706271 D01 Indoor
Q53+Q91+W4
5 Input inspection result
OK
NOK+Reason
Skipped
4 Display inspection items on the glasses
Inspection a, verify the information required to fill out in assembly documents.
Please confirm whether the device is qualified for this inspection item?
1 Scan QR Code on the mark of the device
{
"device_id": "8DN9-2",
"proj_id": 706271,
"bay_id": "D01",
"batch_id": 31302675,
"hzdrawing_page": "HZ-478-M706271-B07",
"transportation_cell_symbol": "Q53+Q91+W4“
}
6 Write inspection results in the database
7 Export inspection results as intermediate table
8 Fill in the FCR with corresponding data
9 Adjust the FCR
(Format, Content, etc.)
10 Finish
Scan
API
Photo that contains the QR Code
Decoded information
Input
Output
API
Database
Table
Input
Inter-mediate
CozeCode
CozeCode
Python
FCR
Output
Device Model | Insp. Id | Insp. Item
8DN9-2 | a | Verify the information required to fill out in assembly documents.
8DN9-2 | b | Check the consistency of assembly and technical drawing
8DN9-2 | … | …

## Slide 12: 3 Project Progress Demo
Start Inspection.
Device scanned. Added values: Project No. 706271, Bay D01, Modules Q8+Q9+W1
Inspection a, <Display the inspection here>.
Please confirm whether the device is qualified for it?
Qualified.
Not Qualified.
Skip this item.
Qualified.
Not Qualified.
Skip this item.
Skip this item.
This inspection item has been recorded and marked as Skipped.
Qualified.
Not Qualified.
Skip this item.
Not Qualified.
What is wrong with this inspection: <Display the inspection item>
<Problem description.>
This inspection item has been recorded and marked as NOK.
Inspection d, check whether DS/ES are in the correct state for transport.
Please confirm whether the device is qualified for it?
Qualified.
Not Qualified.
Skip this item.
Qualified.
This inspection item has been recorded and marked as OK.
0 Wake Word
5 Select inspection result
1 Scan QR Code on the mark of the device
2 Save project and device information
3 Load inspection items based on device model
4 Display inspection items on the glasses

## Slide 13: 3 Project Progress Demo
The inspection report has been successfully generated.
The link is https://...
D01
6 Write inspection results in the database
7 Export inspection results as intermediate table
8 Fill in the FCR with corresponding data
9 Adjust the FCR
(Format, Content, etc.)
10 Finish

## Slide 14: 3 Project Progress Future Work
Category | Current State | Future State | What GAMI can provide
User interface | The current workflow relies on a chat-based interface to present inspection tasks and guidance. The interaction is not optimal, as the content is not structured displayed, inspection items are not visually emphasized in the text, and key points may be overlooked. | <card> view, where inspection ID, inspection item and other content are displayed in their own blocks. Visually emphasize the inspection item by making the font bold or bigger. <button> elements for inspection results. | - UI designer
Inspection workflow | The current workflow is designed as a linear workflow. If the process is unexpectedly exited, users must restart and repeat all previously completed inspections from the beginning. | Add save checkpoints and an inspection history retrieval function in the workflow that allow the system to determine whether the inspection has started and where was the last checkpoint. | - Process engineer
Knowledge base | Users cannot access historical inspection records through a knowledge base that summarizes issues identified in previous inspections and their corresponding solutions. As a result, valuable knowledge remains siloed within individual experts rather than being systematically captured and shared. | Build a knowledge base (function already embedded in Rizon) that allows users to ask AI agent during the inspection process by providing contextual recommendations and troubleshooting guidance. | - Data analyst
Image capture | Image capture not integrated in the workflow. Glasses can take pictures, but they can only be transferred to phones via App. No solution for data transfer to computers. | Integrate image transfer to computers in the workflow. The images should be categorized and archived in the server. | - Process engineer
Other reports | The current workflow is primarily designed to generate FCR. The data collected from the inspection has the potential to support the creation of various reports In the department. | Further identify and automate other reporting and business workflows by collaborating with the Quality department. | - Process engineer

## Slide 15: Table of Contents
2
  Background
3
  Project Progress
4
  Other Projects
1
  Introduction

## Slide 16: 4 Other Projects
Task | AI-assisted information summarization and key point extraction | 
Features | An agent which retrieves and answers company-relevant internal information based on RAG (Retrieval-Augmented Generation). | 
Methods | 1. Collect relevant documents and knowledge. | e.g. internal and external standards, instruction files, history corrective action, photos, etc.
 | 2. Set up the knowledge base. | Save those documents in the knowledge base by semantic segmentation and data vectorization
 | 3. Specify the retrieval workflow. | Specify the agent workflow by writing the agent.md file. Verify whether the recall slice of the knowledge base content is correct or not.

## Slide 17: 4 Other Projects
Task | AI-assisted screening and abnormality warning of quality inspection record | 
Features | An agent which utilizes quality tools to analyze and understand the trend of key quality points and issue early warnings for non-conformance (NC). | 
Methods | 1. Digitalize and automate the entry of monitoring data at these quality points (if possible). | Set up the pipeline for data entry.
 | 2. Use various quality tools to keep track on the quality trend. | e.g. SPC (Statistical Process Control)
 | 3. Set up the agent workflow to automatically analyze data and issue warnings. | Integrate the analysis process (e.g. SPC) into the agent workflow. Specify standard value and tolerance. Also specify when, what and how to inform when NC occurs.

## Slide 18: 4 Other Projects
Task | Machine-Vision-based automatic Gas Insulated Switchgear (GIS) inspection | 
Features | A machine vision model which detects the surface finish and other appearance features of a Gas Insulated Switchgear (GIS) with high accuracy and efficiency. | 
Methods | 1. Specify the inspection check list for each model. | (Concept) Three level of defects detection First level: surface finish Second level: labels and painting color Third level: structural conformance to the drawing
 | 2. Collect training data and train the machine vision model. | 
 | 3. Deploy several robot arms equipped with high-resolution cameras. | Specify inspection points/routes for each module.
 | 4. Validate its accuracy at inspection. |